## Slide 1: ET0023 Operating Systems
10. Disk Storage

## Slide 2: Size Matters
Bill Healy, executive vice president at Hitachi, holds up a platter from a 1-inch microdrive in his
right hand. In his left is a 24-inch platter from IBM's RAMAC (Random Access Method of
Accounting and Control), which came out 50 years ago. A 1-inch 8GB platter holds more than
80,000 times as much data as a single 24-inch RAMAC platter. An 8GB 1-inch drive holds 1,600
times as much data as RAMAC.
Credit: Michael Kanellos, CNET News.com (http://asia.cnet.com/hard-drive-hits-the-big-five-zero-39434750.htm)

## Slide 3: Internal Structure

## Slide 4: Sectors and tracks
Data is stored on the surface of a platter in sectors along the tracks.
Tracks are concentric circles on the disk.
And sectors are part portion of a track.

## Slide 5: Magnetic Storage Terms
A disk consists of one or more metal/glass platters which may be accessed on 1 or 2 surfaces.
Each platter is divided into a number of concentric tracks.
A cylinder is made up of a track on each of the platters at the same horizontal position.
Each track is divided into sectors which usually hold 512 bytes of user data.
Outside tracks (OD)may hold more information than inside tracks (ID) on a platter.
The platters spin at a high speed measured in RPM.
Seek time is the time taken for the Read/Write head to move from one track to another for information.
The amount of data that the drive can read/write per second is known as the data access rate.
Notes: How many sectors are there in 1 Mega byte of user data?
No. of sector = 1024000 / 512 = 1000 K / 0.5 K = 2000 sectors

## Slide 6: Overheads
To read from disk, we must specify:
  cylinder #, surface #, sector #, transfer size, memory address
  CHS and LBA scheme
  Transfer time: get bits off the disk to computer
Transfer time includes:
  Seek time: to get to the track
  Latency time: to get to the sector
Sector
Track
Seek Time
Rotation
Delay
Notes: What is the time of one revolution of the disk for 7200 RPM drive?
No. of rev per second = 7200 / 60 = 120
time per rev = 1000 /120 ms = 8.33 ms

## Slide 7: Access time
Access time = Seek time + Latency time + Overheads
What is the time of one revolution of the disk for 7200 RPM drive?
No. of rev per second = 7200 / 60 = 120
time per rev = 1000 /120 ms = 8.33 ms
Latency time = ½ of rev time = 4.17 ms
Access time = 7 ms + 4.17 ms + 0.5 ms =~ 12 ms

## Slide 8: Modern Disk Drives
 | Seagate Barracuda 7200.12 | Seagate Cheetah 15K7
Capacity | 1 TB | 300 GB
Disk/Heads | 1/2 | 2/4
Cache | 32 MB | 16 MB
Speed | 7200RPM | 15000RPM
Latency (ms) | 4.16 | 2.0
Avg seek (ms) | 8.5/9.5 | 3.4/3.9
Avg data rate (MB/s) | 156 | 600
Interface | SATA 3GB/s | 6 GB/s SAS

## Slide 9: Disk Structure
Disk drives addressed as 1-dim arrays of logical blocks (the smallest unit of transfer)
This array mapped sequentially onto disk sectors
Address 0 is 1st sector of 1st track of the outermost cylinder
Addresses incremented within track, then within tracks of the cylinder, then across cylinders, from innermost to outermost
Translation is theoretically possible, but usually difficult
Some sectors might be defective
Number of sectors per track is not a constant

## Slide 10: Disk Sectors / Track
Reduce bit density per track for outer layers (Constant
Linear Velocity, typically HDDs)
• Have more sectors per track on the outer layers, and
increase rotational speed when reading from outer
tracks (Constant Angular Velocity, typically CDs, DVDs)

## Slide 11: Disk Scheduling
The operating system tries to use hardware efficiently
  for disk drives having fast access time, disk bandwidth
Access time has two major components
  Seek time is time to move the heads to the cylinder containing the desired sector
  Rotational latency is additional time waiting to rotate the desired sector to the disk head.
Task: Minimize seek time
Seek time » seek distance
Disk bandwidth is total number of bytes transferred, divided by the total time between the first request for service and the completion of the last transfer.
Different algorithms exist for addressing this problem.

## Slide 12: Disk Scheduling Algorithms
First-Come-First-Served
Shortest-Seek-Time-First
SCAN | starts at one end of disk, moves to the other end, servicing requests, reverses repeating action
C-SCAN | starts at one end of disk, moves to the other end, servicing requests, returns to start position
C-LOOK | Actuator arm only goes as far as last request in each direction, then reverses

## Slide 13: Good Algorithms
Performance depends on number and types of requests
Requests for disk service can be influenced by the file allocation method.
Disk-scheduling algorithm should be a separate OS module (replacement is possible)
Choices:
  SSTF is common and has a natural appeal
  SCAN and C-SCAN perform better under heavy load
  Either SSTF or LOOK is a reasonable default algorithm

## Slide 14: Low-level Disk Formatting
After manufacturing disk has no information
  Is stack of platters coated with magnetizable metal oxide
Before use, each platter receives low-level format
  Format has series of concentric tracks
  Each track contains some sectors
  There is a short gap between sectors
Preamble allows h/w to recognize start of sector
  Also contains cylinder and sector numbers
  Data is usually 512 bytes
  Error Correction Code (ECC) field used to detect and recover from read errors
Preamble | Data | ECC

## Slide 15: Cylinder Skew
Rotation speed: 10000 rpm
  Drive rotates in 6 ms
  Track has 300 sectors
  New sector every 20 μs
  If track seek time 800 μs
  40 sectors pass on seek
Cylinder skew: 40 sectors

## Slide 16: Formatting & Performance
If 10K rpm, 300 sectors of 512 bytes per track
  153600 bytes every 6 ms 24.4 MB/sec transfer rate
If disk controller buffer can store only one sector
  For 2 consecutive reads, 2nd sector flies past during memory transfer of 1st track
  Idea: Use single/double interleaving

## Slide 17: Disk Partitioning
Each partition is like a separate disk
Sector 0 is MBR
  contains boot code + partition table
  Partition table has starting sector and size of each partition
High-level formatting
  Done for each partition
  Specifies boot block, free list, root directory, empty file system
What happens on boot?
  BIOS loads MBR, boot program checks to see active partition
  Reads boot sector from that partition that then loads OS kernel, etc
Modern PC OS have 4 partitions (3 primary, 1 extended)

## Slide 18: Disk Partitioning Software
Using windows Disk Management or CLI Fdisk.exe

## Slide 19: GNU GParted

## Slide 20: Typical Windows Partitions
500GB Disk
100GB | 200~250GB | 100GB | 16GB
Win OS
Data
Images /
restore point
Swap
500GB Disk
100GB | 
Primary
Extended Logical Drives
200~250GB | 100GB | 16GB

## Slide 21: Typical Linux Partitions
A Linux system consists of
  root (/)
    tmp for temporary files
    var for files that change
    usr for system files and programs
  /home
    User home directories
  Swap
Partitions are usually created for each, though newer systems use Logical Volumes

## Slide 22: What happens if a disk is bad?
A disk track with a bad sector
Solutions:
  Substitute a spare for the bad sector (sector sparing)
  Shift all sectors to bypass bad one (sector forwarding

## Slide 23: Speed vs Data Integrity
Disks are improving, but not as fast as CPUs
  1970s seek time: 50-100 ms.
  2000s seek time: <5 ms.
  Factor of 20 improvement in 3 decades
We can use multiple disks for improving performance
  By Striping files across multiple disks (placing parts of each file on a different disk), parallel I/O can improve access time
Striping reduces reliability
  100 disks have 1/100th mean time between failures of one disk
So, we need Striping for performance, but we need something to help with reliability / availability
To improve reliability, we can add redundant data to the disks, in addition to Striping

## Slide 24: Striping
Data to be written
A | B | C | D | E | F | G | H | I | J | K | L
Striping Disk Device
A | B | C
D | E | F
G | H | I
A
D
G
C
F
I
B
E
H

## Slide 25: RAID
Redundant Array of Independent Disks
Motivation
  Disk drives are small and cheap, can replace large disks with an array
  Requires a RAID controller
  Can put in striped data plus redundancy information
Alternatives:
  SLED (Single Large Expensive Disk)
  JBOD (Just a Bunch Of Disks)
  SPAN (concatenation of disks)

## Slide 26: RAID Issues
Granularity
  fine-grained: Stripe each file over all disks. This gives high throughput for the file, but limits to transfer of 1 file at a time
  coarse-grained: Stripe each file over only a few disks. This limits throughput for 1 file but allows more parallel file access
Redundancy
  uniformly distribute redundancy info on disks: avoids load balancing problems
  concentrate redundancy info on a small number of disks: partition the set into data disks and redundant disks

## Slide 27: RAID 0
Level 0 is non-redundant disk array
Files are Striped across disks, no redundant info
High read throughput.
Best write throughput (no redundant info to write)
Any disk failure results in data loss
  Reliability worse than SLED
RAID 0 – Blocks Striped, No Mirror, No Parity
A
D
G
C
F
I
B
E
H

## Slide 28: RAID 1
Mirrored Disks
Data is written to two places
  On failure, just use surviving disk
On read, choose fastest to read
  Write performance is same as single drive, read performance is 2x better
Expensive
RAID 1 – No Stripe, Mirror, No Parity
A
B
C
A
B
C
Disk
Mirror

## Slide 29: RAID 5
Minimum 3 disks.
Good performance (as blocks are striped).
Good redundancy (distributed parity).
Best cost effective option providing both performance and redundancy.
Use this for DB that is heavily read oriented. Write operations will be slow
P0
P2
E
B
D
F
A
C
P1
RAID 5 – Blocks Striped, No Mirror, Distributed Parity

## Slide 30: Parity & Hamming Codes
Parity
  Detect a single error
  Cannot tell you which of the bits is in error
Hamming codes
  Detect double bit errors
  Detect & correct single bit errors
  Detection and correction require more work
Error Correcting Codes
  Introduce redundancy into data
  Able to detect and correct N errors

## Slide 31: RAID 6
Block level striping with double distributed parity.
Can tolerate 2 hard disk failures
Faster than RAID 5 on read
Slower on writes
Essential in today's large capacity drives

## Slide 32: What about RAID 2,3,4 ?
RAID 2
  bit level striping with ECC codes for error correction.
  Requires many disks (data + ECC).
  Complicated
RAID 3
  Uses a parity disk (holds parity of corresponding bits on other drives)
  Read accesses all data disks
  Write accesses all data disks and parity
  Use parity disk to compute missing data
RAID 4
  Combines RAID 0 and 3
  Block level parity with striping
  Heavy load on the parity disk
Theoretical,
Not used

## Slide 33: RAID 0 + 1
Uses 2 disk arrays
  Array 1 runs in RAID 0
  Data is block-striped across this array
  Array 2 is a mirror of Array 1
C
F
I
B
E
H
A
D
G
C
F
I
B
E
H
A
D
G
DATA

## Slide 34: RAID 1 + 0 (10)
Uses 2 disk arrays
  Array 1 and 2 runs in RAID 0
  Each drive in Array 1 is mirrored to Array 2
  On a drive failure, only faulty drive is replaced
C
F
I
B
E
H
A
D
G
C
F
I
B
E
H
A
D
G
DATA

## Slide 35: RAID Controllers
Hardware RAID
  Most common method of implementing Industry-standard RAID
  hardware controllers e.g. Adaptec, Intel
  Advantages
    Dedicated hardware for striping, parity
    Data caching
    Improved speeds on read/write
Software RAID
  MS Windows built into Disk Management
  Linux: mdadm utility
  Advantages
    Common platform, not hardware dependent
    Cheap
    Modern day CPUs are fast enough to handle processing

## Slide 36: CD-ROM
Spiral makes 22,188 revolutions around disk (approx 600/mm).
Will be 5.6 km long. Rotation rate: 530 rpm to 200 rpm

## Slide 37: CD-ROM Layout
Logical data layout on a CD-ROM

## Slide 38
QUESTIONS

## Slide 39: Head Disk Coupling Field
Magnetic flux
v
d
d
g
Head gap fringing field
g=gap size d=flying height d=magnetic layer thickness v=surface velocity

## Slide 40: Perpendicular Magnetic Recording
Direction of Medium Travel
Electrically Conductive Coil
Perpendicular Recording Head
Magnetic Head reflection
Recording Medium
“Soft” Magnetic Layer

## Slide 41: Areal Density
Magnetic pattern written on disk media
Current areal density, tpi, bpi?

## Slide 42: Low Level Formatting
Before you can write data to a disk, you must first low level format the disk. In this process, the drive manufacturer marks the tracks and sectors of the disk.
An OS will perform a high level format to organize the disk into clusters for file storage. A cluster consists of several sectors.
Track
Sector
Cluster

## Slide 43
8
Head Disk Interface

## Slide 44: Head Flying Height

## Slide 45: Ramp load/unload dynamics
www.hitachiGST.com

## Slide 46
What is access time?
Amount of time device takes to locate data
Considerations
  access time
  cost per megabyte
  volatility
  capacity
  portability
Memory (RAM)
Compact Disc
Tape
SSD
Hard Disk
cost
less expensive
more expensive
speed
faster
slower

## Slide 47: Optical Memory
High capacity
  CD – 650 MB
  DVD – 4.7 GB ~ 17 GB
Slow access time ~ 100 ms
Slow transfer rate
  1X = 150 KB/s
  40X = 40 * 150 KB/s = 6 MB/s
Low cost media
Non-Volatile
Removability – Easy to carry
Built in dust protection
Reliability – non-contact operation, no wear/friction

## Slide 48: How a DVD Drive Works

## Slide 49: Solid State Memory SSD
Flash drive (EEPROM)
Fast access time
Non-volatile
Small physical size
  Easy to carry
Ruggedness and good durability
low power consumption
  little heat generation
  quiet operation
Many incompatible formats
  lack of storage capacity
  Expensive but price coming down fast

## Slide 50: NAND Flash
NAND flash leverages electron tunnelling to store charges onto floating gates
Charge storage creates voltage that is sensed – cell becomes programmed

## Slide 51: SLC versus MLC
SLC stores one bit per cell
MLC utilizes multiple voltage states to store two or more bits per cell.
lower cost at higher data density
Reference point
Reference point
SLC
SLC
Notes: In single-level cell (SLC) NAND flash technology, each cell can exist in one of two states, storing one bit of information per cell. Most MLC NAND flash memory has four possible states per cell, so it can store two bits of information per cell. This reduces the amount of margin separating the states and results in the possibility of more errors. Multi-level cells which are designed for low error rates are sometimes called enterprise MLC (eMLC).

## Slide 52: Incursion of SSD in HDD Markets
Enterprise systems and servers
  Fewer SSD with high IOPS at low power consumption.
  Multiple high capacity but cheaper HDDs is still needed.
Notebooks and Tab
  Lower storage capacities favours SSDs.
  SSDs are more costly than HDDs,
  Fast start up and always on
Notes: Two HDD market segments are exposed to future SSD incursion
  SSDs achieve high IOPS at low power consumption.
  High displacement ratio of one SSD to multiple HDDs
  Higher capacity, cheaper HDDs will still be needed.
  Need lower storage capacities and are therefore a target market for SSDs.
  SSDs can cost 10 times more per gigabyte than HDDs,
  Convenience in file transfer

## Slide 53: SSD 2.5" vs HDD 2.5"

## Slide 54: Activity: Alternative Memory Devices
54
 | DRAM | HDD | DVD
Speed |  |  | 
Capacity |  |  | 
Price |  |  | 
$/GB |  |  | 
Usage |  |  |